## Slide 1: Spokane River PCB Source Assessment
Washington State Department of Ecology
Spokane River Forum May 24 2011

## Slide 2: Spokane River Total PCBs in Fish Tissue 1993-1999
ng/g= parts per billion
Chart: Total PCBs (ng/g, wet)
| Plant Ferry | Ninemile
Trout Fillet | 758 | 270
Whole Suckers | 837 | 745
Max
Min
Mean
WA Standard= 5.3 ng/g

## Slide 3: Components of Spokane River PCB Source Assessment
Source Assessment 2003-2004
Fish Tissue Advisory Update 2005
City of Spokane Stormwater 2007

## Slide 4: Sampling Overview
Sampling conducted between 2003 - 2007
River water (2003-04)
Industrial and municipal discharges (2003-04)
Storm water (2007)
Bottom sediments and sediment cores (2003-04)
Suspended particulates (2003-04)
Resident fish (2005)
Rainbow and Brown Trout, Mountain Whitefish, Smallmouth Bass, Largescale and Bridgelip Sucker

## Slide 5: Study Area
RM 0
RM 112

## Slide 6: Historic PCB Effluent Loading Data 1994-2002
Discharge | 1994 | 1995 | 2000 | 2001 | 2002
Kaiser Trentwood | 2300 | 2600 | 2400 | 480 | 140
Spokane WWTP | - | - | - | 260 | -
Inland Empire Paper | - | - | - | 40 | 94
Liberty Lake WWTP | - | - | - | 4.3 | -
-=Not measured
milligrams/day

## Slide 7: Comparison of WWTP Effluent Concentrations of PCBs in Washington
Chart: Total PCBs (pg/l)
| Everett | City of Tacoma | King County West Point | Chambers Creek | Shelton | Yakima (18 Plants) | Spokane | Walla Walla | Bremerton | Liberty Lake
TPCBs (pg/l) | 15600 | 4700 | 1800 | 910 | 580 | 578 | 536 | 380 | 330 | 282
pg/l= parts per quadrillion

## Slide 8: PCB Loads from City of Spokane Storm Drains
Total PCB Load= 690 mg/day

## Slide 9: PCB Loading in Spokane River 2003-2004
City of Spokane Stormwater= 690
Idaho
Washington
Monroe Street Upper Falls Dam
(RM 74.5)
Ninemile Dam (RM 58.1)
477
Stateline (RM 96.1)
Liberty Lake WWTP= 2.9
Little Spokane River= 97
Kaiser= 65= 65
354 (mid)
721 (bottom)
Upriver Dam (RM 80.2)
Inland Empire= 45
Long Lake Dam
(RM 33.9)
1,413
2,281
3,664
Spokane WWTP= 194
Flow
Total PCBs, mg/day
Source | Load (mg/day)
City of Spokane Stormwater | 690
Stateline | 477
Spokane WWTP | 194
Little Spokane River | 95
Kaiser | 65
Inland Empire Paper | 45
Liberty Lake WWTP | 2.9

## Slide 10: Distribution of PCB Sources 2003-2004
Chart: 
| Municipal/Industrial | Stormwater | Idaho | Little Spokane River
 | 20 | 44 | 30 | 6

## Slide 11: Dissolved PCBs in Mainstem 2003-2004
pg/l= parts per quadrillion

## Slide 12: Reductions Needed In Spokane River to Meet Water Quality Standards
Location on Spokane River | Current t-PCB Load (mg/day) | Target t-PCB Load (mg/day) at Water Quality Criterion |  | t-PCB Load Reduction Required to Meet Water Quality Criterion | 
 |  | NTR (170 pg/l) | Spokane Tribe (3.37 pg/l) |  | 
 |  |  |  | NTR | Spokane Tribe
Stateline | 477 | 766 | 15 | none required | 97%
Upriver Dam | 537 | 780 | 15 |  | 97%
Monroe St. | 1,413 | 1,208 | 24 | 15% | 98%
Ninemile | 2,281 | 1,243 | 25 | 46% | 99%
Little Spokane River | 97 | 83 | 2 | 15% | 98%
Lake Spokane (lower) | 3,664 | 1,562 | 31 | 57% | 99%
Little Falls | 3,664 | 1,562 | 31 | 57% | 99%
Spokane Arm | 3,664 | 1,562 | 31 | 57% | 99%

## Slide 13: Total PCBs in Spokane River Sediments
Chart: Total PCB Concentration (ng/g OC)
| Monroe St | Little Spokane R | Upper Lake Spokane | Middle Lake Spokane | Lower Lake Spokane | Little Falls | Spokane Arm | Buffalo Lake (Ref)
t-PCB (ng/g OC) | 1714.5167 | 242.9294 | 1774.7857 | 813.1433 | 933.3014 | 311 | 610.9006 | 34.9041
ng/g, OC= parts per billion organic carbon normalized

## Slide 14: Sediment Effects at Upriver Dam 2003-2004
pg/l= parts per quadrillion
Dissolved Total PCBs in Surface Water

## Slide 15: Sediment Profile for Lower Lake Spokane
ng/g= parts per billion
Steep declines from 1960s through mid-1980s
Concentrations have decreased by about ½ since mid- 1980s

## Slide 16: PCBs in Spokane River Fish 2005
Sportfish Fillets
Whole Suckers
Highest Levels near Mission Park
ug/kg= parts per billion

## Slide 17: Total PCB Levels in Freshwater Fish from WA. 2001 to 2008
Chart: Percentile (n=303)
Spokane River 2005 | 280 | 220 | 220 | 203 | 190 | 172 | 160 | 130 | 130 | 129 | 121 | 120 | 118 | 94 | 86 | 82 | 78 | 71.2 | 70.2 | 68 | 58 | 55 | 49 | 48.6 | 48 | 45.7 | 41 | 38.4 | 36.9 | 36 | 33.5 | 16.3 | 9.6
t-PCBs Background Study | 98 | 42 | 24 | 11.4 | 8.8 | 7.27 | 6.5 | 6 | 4.9 | 4.1 | 3.84 | 3.7 | 3.43 | 3.01 | 2.1 | 1.99 | 1.9 | 1.7 | 1.7 | 1.6 | 1.6 | 1.3 | 1.3 | 1.3 | 1.28 | 1.21 | 1.2 | 1.17 | 1.1576 | 1.143 | 1.1 | 1.04 | 1.01 | 0.9109 | 0.83 | 0.707 | 0.53 | 0.447 | 0.35 | 0.31 | 0.29 | 0.26 | 0.25 | 0.248 | 0.23 | 0.044 | 0.044

## Slide 18: Conclusions
PCB levels in Spokane River have declined since 1990s but are still above standards and elevated compared to most other areas of Washington
PCB concentrations in water increase moving downstream from the Idaho border to Lake Spokane
The largest PCB loading to the river appears to be from storm water in the City of Spokane
To meet the Spokane Tribe water quality standard, all sources (including the river at the Idaho Border and sediments) will have to be reduced by at least 95%

## Slide 19: Recommendations
Implement Spokane River Toxics Reduction Strategy
Prevention, management and cleanup
Conduct upstream source tracing within conveyance systems
Urban Waters Initiative
Conduct effectiveness monitoring to track progress in reducing PCB levels
Draft plan scheduled for early 2012

## Slide 20: Links
Spokane River PCB Source Assessment 2003-2007
http://www.ecy.wa.gov/biblio/1103013.html
Spokane River Toxics Reduction Strategy
http://www.ecy.wa.gov/biblio/1110038.html