## Slide 1: In-Water Regulatory Drivers
Spokane River

## Slide 2: Summary of Category 5 Section (303d)Toxics Listings for the Spokane River, 2008 List
Reach | Chemical
Spokane River- Idaho border to Ninemile Dam | PCBs, Dioxin, Lead
Little Spokane River | PCBs
Lake Spokane (Long Lake) | PCBs, Dioxin
Spokane River- Below Lake Spokane Dam | PCBs, Dioxin

## Slide 3: Summary of PCB Standards
Regulation or Guidance | Aquatic Life - Water |  | Human Health bc |  | Fish Tissue Consumption Rate (g/day)
 | chronic (pg/l) | Acute (pg/l) | Water (pg/l) | Tissue (ng/g) | 
Washington Water Quality Standards (Ch. 173-201A WAC) | 14,000 | 2,000,000 | - | - | -
National Toxics Rule (40 CFR 131) | - | - | 170 | 5.3 | 6.5
Spokane Tribe Water Quality Standards (Resolution 2003-259) | 14,000 | 2,000,000 | 3.37 | 0.1 | 86.3
National Recommended Water Quality Criteria (EPA, 2002) | - | - | 64 | 2.0 | 17.5
Upriver Dam MTCA Sediment Cleanup Value | 62 ug/kg | - | - | - | -
pg/l= parts per quadrillion
ug/kg= parts per billion

## Slide 4: Water Quality Criteria for PCBs
Washington State
Human Health (EPA National Toxics Rule)
  170 ppq (parts per quadrillion) in water
    6.5 grams per day consumption rate
    Translates to 5.3 ppb (parts per billion) for fish tissue
Spokane Tribe
Human Health
  3.37 ppq in water
    86.3 grams per day consumption rate
    Translates to 0.1 ppb for fish tissue

## Slide 5: PCB Levels in Freshwater Fish from Washington 2001 to 2008
Chart: Percentile (n=303)
Spokane River 2005 | 280 | 220 | 220 | 203 | 190 | 172 | 160 | 130 | 130 | 129 | 121 | 120 | 118 | 94 | 86 | 82 | 78 | 71.2 | 70.2 | 68 | 58 | 55 | 49 | 48.6 | 48 | 45.7 | 41 | 38.4 | 36.9 | 36 | 33.5 | 16.3 | 9.6
t-PCBs Background Study | 98 | 42 | 24 | 11.4 | 8.8 | 7.27 | 6.5 | 6 | 4.9 | 4.1 | 3.84 | 3.7 | 3.43 | 3.01 | 2.1 | 1.99 | 1.9 | 1.7 | 1.7 | 1.6 | 1.6 | 1.3 | 1.3 | 1.3 | 1.28 | 1.21 | 1.2 | 1.17 | 1.1576 | 1.143 | 1.1 | 1.04 | 1.01 | 0.9109 | 0.83 | 0.707 | 0.53 | 0.447 | 0.35 | 0.31 | 0.29 | 0.26 | 0.25 | 0.248 | 0.23 | 0.044 | 0.044